## Slide 1: Transcranial Magnetic Stimulation Chris Chambers CUBRIC Head of Brain Stimulation

## Slide 2
Logic of Neurostimulation
Changes in behaviour that result from stimulation of brain activity can tell us about the causal role of that activity
 | Independent Variable | Dependent Variable | Inference
Neuroimaging | Behaviour | Brain activity | Which brain activity is associated with which behaviour
Neurostimulation | Brain activity | Behaviour | Which brain activity is necessary for which behaviour

## Slide 3
Thompson, 1910
Magnusson &
Stevens, 1911
Barker, 1985
Faraday, 1831
Arsenne d’Arsonval, 1896
Electromagnetic induction
History

## Slide 4
Transcranial Magnetic Stimulation

## Slide 5
Physics of TMS
TMS exploits Faraday’s law of electromagnetic induction
TMS activates neurons
it can suppress/enhance perception, elicit phosphenes, alter cortical excitability; useful tool for studying localization of brain function and neural connectivity
also has clinical applications: treatment of depression, epilepsy, migraine, tinnitus
A time-varying magnetic field induces an electric field, which in turn drives currents in any nearby conductive material
Wagner et al. (2009) Cortex, 45, 1025-1034

## Slide 6
Anatomical Resolution
Difficult and frequently-asked question
  the brain is a complex and non-uniform conductor
Anatomical resolution can be assessed locally and remotely
  Local effects
    beneath the centre of the TMS coil
    3D Gaussian function describing likelihood of the induced electric field directly activating a neuron
Influenced by several interactive parameters:
  Coil shape
  Coil size
  Coil orientation and direction of current flow
  Output Intensity (magnetic flux density in Tesla)

## Slide 7
Anatomical Resolution
Coil shape: determines shape of induced electric field
Figure-of-eight coil

## Slide 8
Anatomical Resolution
Coil shape: determines shape of induced electric field
Round coil

## Slide 9
Anatomical Resolution
Coil size
  smaller coil = smaller electric field = increased focality

## Slide 10
Anatomical Resolution
Coil orientation
  determines the direction of the induced current
  relationship between current direction and local cytoarchitecture will determine the extent of neural firing
  need a trans-membrane current (ion flow) that depolarises the axon membrane and triggers an action potential – fibre bends help
Kobayashi & Pascual-Leone (2003) Lancet Neurology 2, 145-156.

## Slide 11
Anatomical Resolution
Thielscher & Kammer (2002). NeuroImage, 17, 1117-1130
Coil orientation
  At a macro level, this influences current spread across millions of neurons that share a similar orientation (e.g. in M1)
Output Intensity
  greater intensity = reduced focality
  effective intensity is also determined by scalp-cortex distance

## Slide 12
Remote effects (activity beyond the induced field arising from connectivity)
Depend on all of the factors above, plus functional connectivity
Anatomical Resolution
Figure from Ilmoniemi et al. (1997). NeuroReport, 8, 3537-3540

## Slide 13
Anatomical Resolution

## Slide 14
Anatomical Resolution
‘Functional focality’ can be inferred from the effects of TMS
e.g. motor cortex mapping, comparison of behavioural performance between adjacent brain regions
Conclusion: Physical principles provide only a very general indication of focality
  TMS directly stimulates cortex only (max 2-3 cm depth)
  It may directly stimulate (0.5) – (2.5)3 cm of cortical tissue, depending on cytoarchitecture, coil size, coil shape, coil orientation, stimulation intensity

## Slide 15
Temporal Resolution
Depends how resolution is measured, how and where TMS is applied, and strength of the induced electric field
EEG measurements suggest that brain activity induced by a single TMS pulse may be altered for up to 600 ms, both locally and remotely
Figure from Izumi et al. (1997). Electro. Clin. Neuro., 103, 319-322.

## Slide 16
Temporal Resolution
But the temporal resolution of TMS with respect to behaviour is generally much finer (20-50ms bandwidth)
Ashbridge et al. (1997). Neuropsychologia, 35(8): 1121-31.
Hamilton & Pascual-Leone (1998). TICS, 2, 168-174.
Chambers et al. (2004). Nat Neurosci. 7(3):217-8.

## Slide 17
Technical Continuum of Techniques
Figure from Walsh & Cowey (2000). Transcranial magnetic stimulation and cognitive neuroscience. Nat. Rev. Neurosci., 1, 73-79.

## Slide 18: Neurophysiology
Motor evoked potential (MEP)
Basis of TMS motor threshold

## Slide 19: Neurophysiology
Short intracortical inhibition (SICI) and intracortical facilitation (ICF)
SICI and ICF are intracortical physiological mechanisms revealed by paired-pulse stimulation
Initial conditioning pulse is too weak to cause descending spinal activity – yet still alters sensitivity of cortex to subsequent supra-threshold pulse
SICI – linked to GABAA receptor mechanisms
ICF – linked to glutamatergic NMDA receptor mechanisms